SADC VSAT SUPERVISORY BOARD MEETING

(Gaborone, Botswana, 29 – 31 March 2017)

Agenda Item 7.1 - Operation, maintenance and performance of SADC VSAT II Network

(Presented by ATNS)

SUMMARY This paper summarizes the operation, maintenance and performance of the SADC network.

Reference: Report FRC Call Records Interconnectivity between adjacent Networks Network Availability AFTN cct Availability ATS/DS cct Availability Four level report to ICAO Yearly comparative availability

# INTRODUCTION: Operation and maintenance of the Network

The ATNS Fault Reporting Center continues to provide a 24 hr service. The summary of the calls are given for the period April 2016 to February 2017.

# Discussion

The successful maintenance of the system is achieved through the continuous training, commitment and assistance of member States. The interaction of ATNS staff and local trained Engineers had a positive and beneficial result in terms of minimizing the corrective maintenance trips as well as shortening the outage times of the systems, ensuring the SLA is met. First round of training on the upgraded system is near completion and all member States should have availed staff to be trained.

Occurrences reported to FRC:

Total: FRC            = 162

SADC FRC faults reported (Apr 2016 to Feb 2017)

| Apr May Jun Jul Aug Sept Oct Nov Dec Jan Feb Mar Total FRC 10 15 11 20 21 20 16 16 12 7 14 0 162 Corrective 5 8 8 14 12 14 10 13 9 5 12 110 Preventative 1 0 0 1 2 5 3 2 0 1 1 16 External 4 7 3 5 7 1 3 1 3 1 1 36 Corrective – 110 Preventative – 16 External – 36 |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

Yearly comparative FRC reported call totals

| Year | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Total | 151 | 88 | 87 | 98 | 136 | 210 | 248 | 162 |

The critical units replenished and capacity increased in the stores proved to mitigate long outages during the extension period of the network. All these units have been replaced during this upgrade.

- Multiplexers

- RFT units

- IDUs

Failures of the following non critical units stabilised:

- RF switches

- UPS

The UPS units were replaced during the upgrade where it was identified during the site surveys. All RF switches were replaced.

Interoperability

## Seamless operations, interoperability and interconnectivity between VSAT networks in the AFI Region remains crucial and ATNS remains committed to the best practices.  At present co-operation between ASECNA and ATNS ensures interoperability of the networks.  The specification and design of the NAFISAT and SADC2 network provide continued connectivity with AFISNET and provision was made for the retention of the current technical interface solution with the AFISNET network.

## The retention of the MEMOTEC equipment will serve as capacity to maintain the existing links with the AFISNET Network and insure connectivity from the SADC Network.

ATNS is still experiencing challenges with some of the connections, particularly in respect of the N’Djamena, Niamey and Brazzaville circuits. The obsolescence of the equipment is however becoming a risk and this has been brought to the attention of ASECNA. ASECNA has indicated that all AFISNET MEMOTEC equipment will be replaced by NetPerformer devices. The current Satellite access method will also be investigated.

|  | Availability |
| --- | --- |
| SADC - NAFISAT interconnectivity | 99.98% |
| SADC - AFISNET interconnectivity | 99.96% |

The obtaining of LOI’s, issuing of VISAS and customs processes remain a risk.

# Performance of the Network

Data was collated from April 2016 to February 2017 and is presented to the meeting for information.

PRESENTATION

Network availability

|  |  |  | NETWORK AVAILABILITY |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Jan | Feb | Mar |
| 99.99 | 100 | 99.99 | 99.94 | 100 | 99.94 | 99.88 | 99.98 | 99.81 | 99.91 | 99.96 |  |

Average = 99.95%

AFTN circuit availability

|  |  |  | AFTN CIRCUIT AVAILABILITY |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Jan | Feb | Mar |
| 99.98 | 99.99 | 99.88 | 99.86 | 100 | 99.94 | 99.88 | 99.96 | 99.85 | 99.93 | 99.96 |  |

Average = 99.93%

ATS/DS circuit availability

|  |  |  | ATS/DS CIRCUIT AVAILABILITY |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Jan | Feb | Mar |
| 99.97 | 99.94 | 99.99 | 99.84 | 99.86 | 99.92 | 99.86 | 99.96 | 99.83 | 99.91 | 99.95 |  |

Average = 99.91%

Yearly comparative availabilities

Yearly Network availability

| Year | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Average | 99,93 | 99,99 | 99,99 | 99,98 | 99,94 | 99,9 | 99,93 | 99,97 | 99,95 |

Average = 99.95%

Yearly AFTN availability

| Year | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Average | 98,2 | 98,51 | 99,94 | 99,96 | 99,92 | 99,84 | 99,9 | 99,96 | 99,93 |

Average = 99.91%

Yearly ATS/DS availability

| Year | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Average | 99,78 | 99,89 | 99,97 | 99,97 | 99,87 | 99,79 | 99,9 | 99,94 | 99,91 |

Average = 99.89%

# Four level reporting to ICAO

ATNS provides the VSAT 4 level statistics as required by ICAO on a monthly basis. This is a comprehensive document where space segment, IDU, ODU and end user equipment statistics are collected. Below is an extract of this document for level 1 and 2:

| ES/NO Level |  |  | TX Level dBm |
| --- | --- | --- | --- |
| Antananarivo | 10,8 |  |  |  | Antananarivo | 35 |  |
| Beira | 7,6 |  |  |  | Beira | 36 |  |
| Bujumbura | 11,3 |  |  |  | Bujumbura | 36 |  |
| Dar Es Salaam | 11 |  |  |  | Dar Es Salaam | 37 |  |
| Gaborone | 11,2 |  |  |  | Gaborone | 35 |  |
| Harare | 10,9 |  |  |  | Harare | 36 |  |
| Johannesburg | 13 |  |  |  | Johannesburg | 35 |  |
| Kigali | 12,1 |  |  |  | Kigali | 34 |  |
| Kinshasa | 10,3 |  |  |  | Kinshasa | 34 |  |
| Lilongwe | 9,6 |  |  |  | Lilongwe | 36 |  |
| Luanda | 10 |  |  |  | Luanda | 36 |  |
| Lusaka | 10,5 |  |  |  | Lusaka | 35 |  |
| Manzini | 8,8 |  |  |  | Manzini | 37 |  |
| Maputo | 9,6 |  |  |  | Maputo | 41 |  |
| Maseru | 10,2 |  |  |  | Maseru | 37 |  |
| Plaisance | 9,4 |  |  |  | Plaisance | 38 |  |
| Windhoek | 10,2 |  |  |  | Windhoek | 37 |  |

Level four stats templates for ATS/DS and AFTN services were distributed to all SADC States. ATNS would like to express gratitude to the States that are submitting those stats on a regular basis. Unfortunately feedback with regards to end user outages remains a challenge.

Currently the statistics for SADC are recorded and extracted on the ATNS MMS against the four levels and level 4 stats submissions from States are captured and included in the report.

# Distribution of statistics

Distribution of statistics is done on a monthly basis.

Statistics are published monthly on the ATNS website for State Members to view.  Member states receive an e-mail alert that the statistics are available on the website.

# ACTION TO BE TAKEN BY THE MEETING

The meeting is invited to take note of the above information. More information on specifics will be made available upon request.

States are requested to keep submittting the level 4 statistics recorded on the template to ATNS for the completion of the document to be sent to ICAO.

States are requested to report all SADC network faults to the ATNS FRC on +27 11 928 6477 or frc@atns.co.za and to copy to the Manager ruip@atns.co.za.